## Slide 1
RTOS Overview in Embedded Systems:

## Slide 2
RTOS Name | Type | Key Features | Typical Use Cases | Supported MCU / MPU Architectures
FreeRTOS | Soft RTOS, Monolithic | Lightweight, open-source, portable | IoT devices, small MCUs (STM32, ESP32) | MCUs: ARM Cortex-M (STM32, NXP, TI, Microchip SAM), ESP32, AVR, PIC, RISC-V MPUs: ARM Cortex-A (optional ports)
Zephyr RTOS | Soft RTOS, Microkernel | Modular, secure, supp orts multi-arch (ARM, RISC-V, x86) | IoT, wearables, industrial systems | MCUs: ARM Cortex-M (STM32, NXP, Nordic, TI), RISC-V (SiFive, Espressif), ARC, Nios II MPUs: x86, ARM Cortex-A
VxWorks (Wind River) | Hard RTOS, Hybrid | High reliability, POSIX support, certified for safety-critical systems | Aerospace, defense, automotive | MCUs/MPUs: ARM Cortex-A/R/M, PowerPC, x86, MIPS, RISC-V
QNX Neutrino RTOS | Hard RTOS, Microkernel | Fault isolation, high reliability | Automotive infotainment, medical | MPUs: ARM Cortex-A, x86, PowerPC, MIPS — focuses on MPU-class processors, not small MCUs
Integrity RTOS (Green Hills) | Hard RTOS, Microkernel | Safety-certified (DO-178C, ISO 26262), secure | Avionics, automotive ECUs | MPUs: ARM Cortex-A/R, PowerPC, MIPS, RISC-V MCUs: Some Cortex-M variants for safety-critical control
ThreadX (Azure RTOS) | Firm RTOS, Hybrid | Fast context switching, low memory footprint | Consumer electronics, IoT | MCUs: ARM Cortex-M (STM32, NXP, Renesas, Microchip SAM), RISC-V, MIPS, x86 (limited)
RTEMS (Real-Time Executive for Multiprocessor Systems) | Firm RTOS | Open source, supports POSIX | Space systems (NASA), industrial control | MCUs/MPUs: ARM, PowerPC, SPARC, x86, RISC-V, MIPS — runs on both MCUs and MPUs
Nucleus RTOS (Siemens) | Firm RTOS | Proven, low-power, multiprocessor support | Medical, industrial automation | MCUs/MPUs: ARM Cortex-A/R/M, MIPS, x86, PowerPC
µC/OS-II / µC/OS-III (Micrium) | Soft RTOS, Monolithic | Highly portable, preemptive multitasking | Embedded devices, training systems | MCUs: ARM Cortex-M (STM32, NXP, TI), Renesas RX, 8051, AVR, RISC-V
RIOT OS | Soft RTOS | IoT-focused, supports 6LoWPAN, IPv6 | IoT sensor networks | MCUs: ARM Cortex-M (STM32, NXP, Nordic), AVR, ESP32, MSP430, RISC-V
TinyOS | Event-driven RTOS | Designed for low-power wireless sensor networks | Wireless sensor networks | MCUs: Atmel AVR (ATmega), TI MSP430, ARM Cortex-M3, TelosB motes
RTLinux / Xenomai | Hard RTOS (Linux-based) | Real-time layer under Linux kernel | Robotics, industrial control | MPUs: x86, ARM Cortex-A, PowerPC, RISC-V — runs on Linux-capable processors, not bare-metal MCUs